## Slide 1: Fluid Dynamics Data Acquisition and Tcl
Ron Fox (NSCL/FRIB)
Vaibhav Khane (MU S&T)

## Slide 2: What’s this all about?
Describing the problem.
Describing the software I already had.
Describing the modifications to make it all work.
Some screen shots
Some acknowledgements

## Slide 3: What do we want to do?
Track the flow of ‘fluid particles’ through a complex multi-phase system.
  Multiphase means a mixture of solids, liquids and gasses depending on the type of system.
…and the system is optically opaque.
Large volumes

## Slide 4: Why do we want to do it?
“Multiphase reactors are widely used in petroleum, chemical, petrochemical, pharmaceutical and metallurgical industries as well as in materials processing and pollution abatement….the physical phenomena that affect the fluid dynamics of such systems are not yet entirely understood. This make a priori predictions of important process parameters… very difficult.”
Opaque Multiphase Reactors: Experimentation, Modeling and Troubleshooting.
- M.P. Dudukovich
Oil & gas Science and Technology Rev. IFP V 55 (2000) #2 pp135-158
“Because its fun and you get to play with cool toys”
- Ron Fox 2011

## Slide 5: How do we do it?
Computer Automated Radioactive Particle Tracking (CARPT)
Make ~2mm source of 46Sc (gamma emitter) so that it has neutral boyancy.
  The source will move around in the reactor.
  Track the movement as a function of time.
A typical example is shown at the right:

## Slide 6: How do we do it?
Turns out with some ‘relatively straightforward’ math (left as an exercise for the reader) you can show you just need count rates (intensities)…
…
To find the source position/velocity at any time.

## Slide 7: More algorithmically you want:
There are quite a few difficulties outside the scope
of this paper:
You need good knowledge of detector efficiencies
The detector acceptance is not perfect
If you use a hot source there will be dead time associated with fall time of the signal in the NaI detectors (1uSec).
The contents of the reactor can absorb emitted gamma rays. Attenuation can be difficult to determine/measure (and may be a function of position).

## Slide 8: My Job
Existing electronics
Replace this
Development effort must be cheap
CAMAC

## Slide 9: Replace with This.
List sequencing Crate
Controller Kinetics Systems
3982
-
21 B (1 Kb buffer size)
GPIB Crate Controller
Kinetics Systems 3988
–
63A
AT
-
GPIB Interface
Card National
Instruments
PC under
Windows
Acquisition
program C++
Reads data from
scalers
and interfaces to pc
Collects data and CARPT / CT
analysis
List sequencing Crate
Controller Kinetics Systems
3982
-
21 B (1 Kb buffer size)
GPIB Crate Controller
Kinetics Systems 3988
–
63A
AT
-
GPIB Interface
Card National
Instruments
PC under
Windows
Acquisition
program C++
Reads data from
scalers
and interfaces to pc
Collects data and CARPT / CT
analysis
Linux PC
CC-USB
USB-2

## Slide 10
Remember me from last time we were here?
This project used a USB ↔ VME interface

## Slide 11: Hardware Changes
Linux
Computer
VM-USB
VME Bus
usb-2
Digitizers
external Trigger
Tcl config Files

## Slide 12: Hardware Changes
Linux
Computer
CC-USB
CAMAC
usb-2
Scalers
LE
Discriminators
Timer out
Trigger in
Tcl config Files

## Slide 13: Software Old:
Readout
Data Distribution
Online
Analysis
Detector Rate monitoring
Event recording
But they only need rate monitoring.
At the end of each run they just need a CSV file for their analysis chain

## Slide 14: Software New
Readout
thread
control/analysis
thread
starts
Scaler data events
(Tcl_ThreadQueueEvent)
Tcl Acquisition/analysis scripts

## Slide 15: Acquisition/Analysis modes
Calibration – Run with a source in a known location move the source run some more.
Discriminator setting – Scan the discriminator settings (poor-man’s ADC) to know how to set the threshold.
Production running – Take data for as long as they want to.
Calibration mode
Control/monitoring

## Slide 16: Sample Spectrum from discriminator setting mode.
60Co (1.3, 1.7MeV)
137Cs (661KeV)
Plotchart
Noise

## Slide 17: Conclusions
Modifying the “STUK” readout to be an all-in-one data acquisition system was easy.
Doing the analysis in Tcl provided a lot of flexibility and leveraged:
  The speed of Tcl development
  Ease with which Tk can be used to build user interfaces.
  Plotchart to allow the display of LED threshold data.
At present, position calibration is manual. In the future adding motor control to the application would allow that to be automated.
Having the STUK framework as a starting point allowed this project to be deliverd on the cheap…thanks to the Tcl assist for the analysis control/analysis sections of code..

## Slide 18: Readout Software Structure
Main Thread (Tcl Interp)
Acquisition Thread (Transitory)
starts
Output Thread
Event data
Slow Controls
thread
VME access
management
NSCL DAQ
Control Clients
socket

## Slide 19: Readout software modified for CARPT data taking
Main Thread (Tcl Interp)
Acquisition Thread (Transitory)
starts
Output Thread
Event data
Slow Controls
thread
VME access
management
Scaler data
Tcl Scripts